## Slide 1: Mississippi State Fire Marshal’s Office
Smoke Alarm Installation Training
Tammy L. Peavy
Fire Safety Education Officer

## Slide 2: Advertising
NO give aways-alarms MUST be installed
Newspaper
Radio
TV
Flyers
Sign in sheets
Applications
Door-to-door
Word of mouth

## Slide 3: Make a date
Residents are home
Assistant/caregiver is present
Translator is present

## Slide 4: Interacting with Residents
Address by formal name (Mr., Ms., Mrs., etc.)
Identify yourself clearly
  Wear a name badge
  OR wear organization clothing
  OR go in a marked vehicle
Be persuasive, but respect person’s right to say “no”

## Slide 5: Social Etiquette
Tips for installers who work with people with disabilities

## Slide 6: General Tips
Use “people first” language
Never say “handicapped” or “special”
Never touch or distract a service animal without prior permission
Avoid making assumptions
Don’t be afraid to ask questions.
Try to give people with disabilities options

## Slide 7: General Tips
Disregard the idea that you are saving people with disabilities
A few simple guidelines
  Treat adults as adults
  Don’t be embarrassed if you use common expressions
  Make eye contact with the person who is deaf rather than the translator

## Slide 8: Who gets conventional smoke alarms?
Owner-occupied homes
  No rental property
  No businesses
  No churches

## Slide 9: Who gets conventional smoke alarms?
Owner-occupied homes
Low income families
Older adults
Families with children under 14 years old
People with disabilities

## Slide 10: Recommendations
Remove smoke alarms that are 10 or more years old
Remove non-working smoke alarms
Residents have qualified electrician remove or replace existing hardwired smoke alarms-DO NOT remove them

## Slide 11: Conventional Smoke Alarms
ONLY use alarms provided by the State Fire Marshal’s Office. Do NOT supplement the program with other alarms.
10-year lithium power pack
  No need to replace batteries
Sealed alarm
  Power pack cannot be unplugged or removed
  Power pack will not fit other devices

## Slide 12: Conventional Smoke Alarms
Alarm activates when power cell inserted
Test/silence button
  Used to test alarm
  Allows resident to silence nuisance alarms
  Silences alarm for 10 minutes unless smoke conditions persist

## Slide 13: Testing and Maintenance
Show residents how to test the smoke alarms
Instruct residents to test smoke alarms monthly
Instruct residents to clean smoke alarms monthly with vacuum cleaner soft brush attachment or duster
Show residents how to use the test/silence button
Leave the instructions from the package with the residents
After 10 years or when the alarm starts to chirp, residents should replace the alarm

## Slide 14: Conventional Smoke Alarm Installation
Outside each sleeping area
Inside each sleeping room
On each level of the home, including basement
Areas separated by a door from the required locations

## Slide 15: Conventional Smoke Alarm Installation

## Slide 16: Conventional Smoke Alarm Installation

## Slide 17: Conventional Smoke Alarm Installation

## Slide 18: Conventional Smoke Alarm Installation

## Slide 19: Conventional Smoke Alarm Installation
On ceiling
  At least 4” from wall
            -OR-
On wall
  At least 4” from ceiling
  Not more than 12” from ceiling

## Slide 20: Conventional Smoke Alarm Installation
OR

## Slide 21: Conventional Smoke Alarm Installation

## Slide 22: Conventional Smoke Alarm Installation

## Slide 23: AVOID putting smoke alarms in
Kitchens
Garages
Bathrooms
Areas where temperature or humidity are outside manufacturer’s limits-not below 40F or above 100F (includes most attics)

## Slide 24: AVOID putting smoke alarms
Where mounting surface could become too hot or too cold
Within 3’ of a bathroom or kitchen door
  It is best to install smoke alarms at least 10’-12’ from cooking appliances, where possible
Within 3’ of a supply air register
Within 3’ of air flow path
Within 3’ of ceiling fan blade tips

## Slide 25: Mobile Homes
Many mobile homes built before 1978 have little or no insulation. In these homes or if you are unsure of the age, install smoke alarms on the interior walls only.

## Slide 26: Who gets a SafeAwake alert device?
People who are deaf
People who are hard of hearing
Older adults
May be installed in rental property

## Slide 27: SafeAwake alert device
Activated by conventional smoke alarm T-3 alarm pattern
Emits a high-decibel, low frequency audible signal
White flashing light
Bed shaker
Battery back-up
  Use only CR-123
  lithium batteries
Portable-take it with
  you when you travel

## Slide 28: SafeAwake alert device
Red light
  bed shaker unplugged
Yellow light
  batteries low
Green light
  Solid-on AC power
  Flashing-on battery power

## Slide 29: SafeAwake Testing
Show resident how to test the SafeAwake alarm
Instruct resident to test alarm monthly
  Alarm will alert 30 seconds when triangular button is pressed
  Alarm will alert 2 minutes when conventional smoke alarm is tested for full T-3 signal
Leave the instructions from the package with the resident

## Slide 30: SafeAwake Installation
In every room where a person who is deaf or hard of hearing sleeps
  Also install a conventional smoke alarm in this room

## Slide 31: Who gets a Gentex alarm?
People who are deaf
May be installed in
rental property

## Slide 32: Gentex Alarm
Photo-electric
Strobe light
High frequency audible signal
Battery back up
  Does not operate strobe

## Slide 33: Gentex Alarm Testing
Show residents how to test the smoke alarm
  Turn knob to TEST 1, wait 20 seconds for sound and flash
  Turn knob to NORMAL, wait 20 seconds for sound and flashing to stop
Instruct residents to test smoke alarm monthly
Instruct residents to clean smoke alarm monthly with vacuum cleaner soft brush attachment or duster
Leave the instructions from the package with the residents

## Slide 34: Gentex Installation
In living room/common area near wall outlet that is not controlled by an on/off switch
In any room frequently occupied by a person who is deaf
  Office
  Den

## Slide 35: Provide fire safety and escape planning information
Review all educational handouts with the residents
A fire safety DVD will be provided to people who are deaf or hard of hearing

## Slide 36: Installer Responsibilities
Install alarms according to the Mississippi Fire Marshal’s Office guidelines
Complete a survey/waiver form for each home visited
Every week, mail or deliver all forms to your smoke alarm coordinator

## Slide 37: Distribution
Each organization must have a smoke alarm coordinator
Must return forms showing installation before more alarms distributed
Pick up alarms at distribution point
  Delivery may be possible

## Slide 38: Transfer form

## Slide 39: Transfer
Form must be completed when receiving/distributing alarms
Organization should track number of alarms distributed to each installer

## Slide 40: Forms
Only use forms provided by the State Fire Marshal’s Office-no copies
NO pencils
NO red ink
Write legibly
Check spelling
Do NOT abbreviate organization name

## Slide 41: Corrections
Draw a single line through the error, and write the correct information above, below, or to the side
If you check the wrong box, circle the correct answer
Incomplete forms will be returned

## Slide 42: Waiver Complete 1 per HOUSE

## Slide 43: Name of organization

## Slide 44: Name of community

## Slide 45
Physical address
  Same as on front of form

## Slide 46
PRINT name
  If resident’s writing is illegible, print name for them
Have resident sign form
  MUST be over 18
Date of installation

## Slide 47
If resident is unable to write, have them mark “X”
  Write “His/Her Mark” beside “X”
  Print name
His mark-John Smith X

## Slide 48
PRINT name
  CANNOT be same as resident
Sign
Date of installation

## Slide 49: Survey* Complete 1 per HOUSE *Some forms vary

## Slide 50: Date of installation

## Slide 51
Person installing alarms
  Same on all forms
NOT organization

## Slide 52: Do NOT leave blank

## Slide 53
Include City, State, Zip Code
  Use correct zip code
NO P. O. Boxes
NO Route/Box addresses
If more than one house at same address, write Second House on form

## Slide 54
If same as physical address, write Same as above
Include City, State, Zip Code
  Use correct zip code
NO Route/Box addresses
If more than one house at same address, write Second House on form

## Slide 55
Only used for evaluation
NOT all residents will receive an email

## Slide 56
Include area code
Only used for evaluation
NOT all residents will receive a call

## Slide 57: County where home is located

## Slide 58
Do not leave blanks
  Use “0” or “N/A”

## Slide 59
Permanent residents
  NOT people who frequently say overnight

## Slide 60
Over age 65
NOT the age

## Slide 61
14 years or younger
NOT the age

## Slide 62
Disabilities that would make escape difficult or impossible
  Do NOT include deaf or hard of hearing

## Slide 63: Number of people who are deaf

## Slide 64: Number of people who are hard of hearing

## Slide 65: Number of floors/ stories

## Slide 66
Number of smoke alarms BEFORE you installed
  If “NO”, skip questions 12-18

## Slide 67
If there is only 1 level and 1 existing smoke alarm, this should be “YES”
  If yes, skip #13

## Slide 68: The lowest level of the home above ground is the first floor

## Slide 69: A sleeping area is a room or group of rooms where people sleep

## Slide 70: Include rooms that are not “bed” rooms

## Slide 71: Does not include the alarms you install

## Slide 72
You MUST test all existing alarms
  If you did not, explain why not

## Slide 73: CANNOT be more than #11

## Slide 74: Number of First Alert smoke alarms installed

## Slide 75: Number of Kidde smoke alarms installed

## Slide 76: Number of SafeAwake alarms installed

## Slide 77: Number of Gentex alarms installed

## Slide 78
This is required!
  If no, note why you did not

## Slide 79
This is required!
  If no, note why you did not

## Slide 80: Number of people talked to about handouts

## Slide 81: Questions?